## Slide 1: Multivariable Control
Industrial Robotics – MIEEC@FEUP 2020/2021
António Paulo Moreira1, Paulo G. Costa2, Ricardo B. Sousa3
1Associated Professor of DEEC@FEUP
2Assistant Professor of DEEC@FEUP
3Ph.D. Student of PDEEC@FEUP

## Slide 2: Outline
Dynamics
Multivariable Control
SCARA Manipulator: Practical application of inverse dynamics

## Slide 3: Dynamics
Kinematic equations
  Motion of the manipulator
  No consideration for the forces and torques producing the motion
Dynamics equations
  Motion of the manipulator
  Relationship between forces and motion
How do we consider the dynamics? Euler-Lagrange equations
  Evolution of a mechanical system subject to holonomic constraints
  Based on the principle of virtual work
  Requires the Lagrangian of the system: difference between kinetic and potential energy

## Slide 4: One Dimensional System
Equation of motion :
  Kinetic energy
  Potential energy

## Slide 5: One Dimensional System
Equation of motion :
Lagrangian
  Where and
Euler-Lagrange Equation:
  Goal: describe the motion from the external force (equivalent to the Newton’s 2nd law)
  : external force
  Analysis in terms of kinetic and potential energy

## Slide 6: Single Link Manipulator
(gear ratio )
  : rotational inertia of the motor
  : rotational inertia of the link
  : generalized force that represents the external forces and torques
  , where is the motor torque relative to the link ()

## Slide 7: General Case
, where
System described by the so-called generalized coordinates
  Denavit-Hartenberg joint variables (DH convention)
  DH convention are equivalent to a set of generalized coordinates
Require general expressions for kinetic () and potential () energy

## Slide 8: General Expressions for Kinetic Energy
Concentrate the entire mass of an object at its center of mass
  : total mass of the object
  : linear velocity vector
  : symmetric matrix called the Inertia Tensor (expressed in the inertial frame)
  : angular velocity vector

## Slide 9: Inertia Tensor
  : orientation transformation between the body attached frame and the inertia frame
  : inertia tensor expressed in the body attached frame
is a constant matrix independent of the motion of the object
  Where is the mass density of the object
  Note: if mass distribution is symmetric to the body frame, then inertia cross products are 0

## Slide 10: Inertia Tensor: Uniform Rectangular Solid
Uniform  (constant)
Cross products of inertia are zero

## Slide 11: General Expressions for Kinetic Energy
link robotic manipulator where the joint variables are the generalized coordinates (DH convention)
: mass of link
: inertia matrix of link
  Evaluated around a coordinate frame parallel to frame but whose origin is at the link’s center of mass
: linear velocity vector at the center of mass of link
: angular velocity vector at the center of mass of link

## Slide 12: General Expressions for Kinetic Energy
In matrix form,
  is a symmetric positive definite matrix
  is in general configuration dependent
(see the final slides that present an example of how to compute for the SCARA manipulator)

## Slide 13: General Expressions for Potential Energy
Concentrate the entire mass of an object at its center of mass
  : gravitational vector in the inertial frame
  : coordinates of the center of mass of link in the inertial frame
  Note: the minus sign is required for the potential energy to be correctly computed
if robot contains elasticity (e.g., flexible joints), then potential energy will include terms containing the energy stored in the elastic elements
Potential energy depends on the configuration of the robot but not on its velocity
(see the final slides that present an example of how to compute the potential energy for the SCARA manipulator)

## Slide 14: Equations of Motion
Since :
Euler-Lagrange equation:
  Christoffel symbols of the 1st kind:
    Reduces the computation effort because for a given

## Slide 15: Equations of Motion
In matrix form,
  Where the -th element of the matrix is
  is the influence of the gravity

## Slide 16: Outline
Dynamics
Multivariable Control
SCARA Manipulator: Practical application of inverse dynamics

## Slide 17: Multivariable Control
Previously (independent joint control):
  Single-Input / Single-Output model
  Coupling effects  treated as disturbances
Reality: robot manipulator is a complex, non-linear, multivariable system!
Multivariable Control
  A more rigorous analysis of the performance of control systems
  Design a robust and adaptive nonlinear control laws

## Slide 18: Model of a Revolute Joint
: gear reduction ratio ()
: torque constant (N.m.A-1)
: speed constant (V.s.rad-1)
  Note:
: inertia of the motor (Kg.m2)
: motor viscous constant (N.m.s)
, where and

## Slide 19: Equations of Motion
Motor model:
Euler-Lagrange equation:
  , where is a diagonal matrix with elements
  is a diagonal matrix with elements

## Slide 20: Inverse Dynamics
Goal: nonlinear feedback control () with a linear closed loop system
Outer loop:
  Output of the loop :
  Reference input :
  Gain matrices , : (possible values)
Inner loop:
(see the final slides that present a practical application of inverse dynamics with the SCARA manipulator)

## Slide 21: Inverse Dynamics
Trajectory
Planner
Outer Loop
Controller
Robot
Inner Loop
Controller

## Slide 22: Outline
Dynamics
Multivariable Control
SCARA Manipulator: Practical application of inverse dynamics

## Slide 23: SCARA Manipulator
SCARA: Selective Compliant Articulated Robot for Assembly
Popular manipulator tailored for assembly operations
RRP configuration
Epson SCARA E2L653S
ABB IRB 910SC

## Slide 24: Forward Kinematics (DH convention)

## Slide 25: Forward Kinematics (DH convention)
We will consider that the center of mass of link 3 is align with the end-effector’s coordinate frame

## Slide 26: Forward Kinematics (DH convention)
Link |  |  |  | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 

## Slide 27: Forward Kinematics (DH convention)
Link |  |  |  | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 

## Slide 28: Inverse Kinematics
Note: the inverse kinematics are still require for the inverse dynamics (compute )

## Slide 29: Velocity Kinematics
Matrix defines the velocity kinematics of the end-effector relative to the coordinate frame
However, we can define the velocity kinematics relative to any point of the robot manipulator
Note: the inverse kinematics require the definition of the velocity kinematics of the links’ centers of mass

## Slide 30: Velocity Kinematics
Let us define the forward kinematics of each link’s center of mass :
  
  
  
  Note: is the distance from to the link ’s center of mass (see the initial figure that defines all the coordinate frames)

## Slide 31: Velocity Kinematics
Let us define the forward kinematics of each link’s center of mass :
  
  
  
  Note: is the distance from to the link ’s center of mass (see the initial figure that defines all the coordinate frames)

## Slide 32: Inertia Matrix
For this SCARA manipulator, is a matrix
Also, let’s assume that all three links are a uniform rectangular solid:
  Note: the , , and are relative to the coordinate frame

## Slide 33: Matrix
, where

## Slide 34: Gravity Influence
Note that depends on the direction of the gravity vector in the inertia frame
Horizontal SCARA
Vertical SCARA

## Slide 35: Inverse Dynamics
Outer loop:
  Input of the system :
  Reference input :
  Gain matrices , : (possible values)
Inner loop:
(see the final slides that present a practical application of inverse dynamics with the SCARA manipulator)

## Slide 36: Inverse Dynamics
Trajectory
Planner
Outer Loop
Controller
Robot
Inner Loop
Controller

## Slide 37: Next Steps: Task Space
: end-effector pose using minimal representation of
  Where (analytical Jacobian; see section 4.8 of the book for further details)
Modification: outer loop (the inner loop remains unchanged)
  Note: the task space does not require computing the desired trajectory in the joint space

## Slide 38: Final Observations
Did you thought of doing all the computations for inverse dynamics by hand?
No! For example, use math solvers (MATLAB, Symbolab, etc.) to compute all the matrices required to implement inverse dynamics.
Note: if you use symbolic variables in MATLAB with transposed matrices, it will give you complex numbers:
  MATLAB assumes that the symbolic variable could be a real or a complex number
  So, transposing a matrix, will not only interchange but also switch the imaginary part of each number (conjugate)
  Implement a specific transpose function to only interchange the matrix’s elements (we know that all symbolic variables in the scope of inverse dynamics – etc. – are real numbers)

## Slide 39: References
Spong, M. W., Hutchinson, S., and Vidyasagar, M. 2005. Robot Modeling and Control. 1st edition. John Wiley & Sons.
  Chapter 6: Dynamics
  Chapter 7: Independent Joint Control
  Chapter 8: Multivariable Control

## Slide 40: Multivariable Control
Industrial Robotics – MIEEC@FEUP 2020/2021
António Paulo Moreira1, Paulo G. Costa2, Ricardo B. Sousa3
1Associated Professor of DEEC@FEUP
2Assistant Professor of DEEC@FEUP
3Ph.D. Student of PDEEC@FEUP